EasyMSP Configuration Options
For EasyMSP 1.1.x
# Changing Options
Option can be changed by setting the preprocessor define to ether YES or NO. Using ON and OFF is also acceptable.
## Configuration Location
EasyMSP build time options can ether be set in
- The config.h configuration file
- A custom configuration file
- Program source file.
Set options in the source file if you only changing a few options, otherwise use a configuration file.
Note: Changes made in the config.h configuration file will affect all programs compiled with EasyMSP.
Configuration options in ether a source or custom configuration file must be included before including EasyMSP, otherwise unpredictable results may occur.
# Options

## _EM_ASCII_LOGO
Enable the ASCII logo to appear in the build console. _EM_VERBOSE must be enabled for this option to work.
## _EM_VERBOSE
Display EasyMSP remarks while building in the build console. EasyMSP Verbose mode requires the TI MSP430 C/C++ compiler. This option has no effect in GCC.
## _EM_EASYTYPES
Use easy type definitions such as byte for unsigned char and word for unsigned short int.
## _EM_PREINIT_VECTORS
When enabled, _EM_PREINIT_VECTORS point all unused function vectors to the NULL pointer.
## _EM_SOFTWARE_DELAY
Use software based delays. When Software based delays are used, the MSP430 does not enter any low power modes while delaying. Disabling software delays provides hardware based delays, which can enter low power modes, at the cost of a timer.
## _EM_INIT_BOARD_GPIO
Configures GPIO for on board features such as LEDs and Buttons.