Flash Module Library User Manual
For EasyMSP 1.1.x
DRAFT
UNFINISHED MANUAL – DO NOT USE

# Description
The EasyMSP Flash module library provides functions to abstract the

# User Functions
User function are functions that are intended for use by the API user. Currently there are 1 user functions in total.

## FlashEraseSegment()
Description
flashEraseSegment() erases a speficed flash memory segment. FlashEraseSegment() can operate	on main memory segments, as well as INFO and BSL segments.
This function is ideal for... well erasing any flash memory segment.

## FlashEraseMainMemory()
Description
FlashEraseMainMemory() erases the main program memory. All INFO and BSL segments are	preserved.
This function is ideal for preparing the MSP430 for bootstrap programming.

## FlashNuke()
Description
FlashNuke() is a function to erase all flash memory on the device, including the INFOA segment. After completing this operation, the MSP430 will not be usable until calibration constants and the TLV are reprogrammed on the device.
This function is ideal for erasing sensitive data off the device, while making the device inoperable.

## FlashAppend()
Description
FlashAppend() can append information to existing flash memory segments. FlashAppend()	loads the data contained on the selected flash memory segment, modifies the data in RAM, and	then writes back the data.
But it should be noted that flashAppend() can not be used to append data to main memory	segments in devices with less than 512 bytes of free RAM. However, appending data in the	INFO segments is possible.
Even with this limitation, the Flash module library can work around the limitation by utilizing	info segments B, C, and D to append data 64 bytes a time, up to 192 bytes. The required	memory then to append data will then only be 320 bytes of free RAM, but at the cost of	erasing INFO segments B, C, and D.
Another option is reserving 1 segment (512 bytes) of main flash memory for temporary use.

## flashWrite()

## flashRefresh()
Description
flashRefresh() is used to prevent bit-rot from occurring due to aging.
While the flash cells can endure 100,000 erase/write cycles[1], Flash data will start to “rot” as	soon as 16 years[2] unless the contents of the flash are periodically rewritten.
[1] TI reported typical flash endurance. Minimum specified endurance is 10,000 cycles. See TI's SLAA334A application note for further information.
[2] TI reports that the MSP430 flash data retention time at 50°C is 16 years. Expected flash data retention time at 25°C is about 100 years. See TI's SLAA334A application note for further information.
A typical user should never need to refresh his or hers flash, but if your application is	expected to be exposed to high heat and/or is expected to be operating longer than 35 or more	years, you should refresh your flash periodically (every 15 years is a safe bet). Chances are,	your MSP430 will outlive all other hardware.
Like flashAppend(), flashRefresh() requires a relatively large amount of free RAM (512 bytes).	However, that requirement can be lowered to 320 free RAM bytes at the cost of using INFO	segments B, C, and D as temporary storage.
Another option is reserving 1 segment (512 bytes) of main flash memory for temporary use.
## flashWriteSegment()
## FlashVerify()

# System Functions
System functions are functions that are not intended for use by the API users, but rather by use of the user functions themselves. However, the functions are included for the sake of completeness.

# Preprocessor Defines
## Defines
### SEGMENTA
'A'
### SEGMENTB
'B'
### SEGMENTC
'C'
### SEGMENTD
'D'
### FLASH_KEY1
0xFEEDFACEh in hex or 4277009102 in decimal.
### FLASH_KEY2
0xDEADCODEh
## Return codes
Any return code above 0 indicates an error.
### SUCCESS
The function execution completed without any detectable errors.
### FAILURE
The function did not successfully execute the desired operation. FAILURE is returned when a error occurs and a more specific return code is unavailable.
### INVAILD_KEY
A invalid key was provided, and the operation was aborted.
### SEGMENTS_LOCKED
A flash information segment cannot be erased or written to, because the segment is locked.
### SEGMENTA_LOCKED
The Flash information segment A could not be erased or written to, because the segment is locked in hardware.
### INVAILD_SEGMENT
An invalid segment was provided
### VOLTAGE_CHANGE
The flash erase or write operation failed to due a change in the device voltage. The result of the operation is unpredictable.
### FLASH_BUSY
The flash memory controller is busy and cannot process another request.
### FLASH_FAILURE
The flash memory segment has failed.
### BAD_CLOCK
The flash memory controller can not perform a write or erase due to a system clock failure.

# Global Variables
No global variables exist in the Flash Library.

# Appendix A – Remarks
The
## Resource usage
The EasyMSP Flash library uses a considerable amount of on chip resources. Only a small amount of free RAM is required (less than 30 bytes) for erase and write operations. Append operations require much larger amounts, typically upwards of 512 or more bytes of free RAM.
## Appending limitations
While the EasyMSP flash library has operations for appending data to flash, Appending data to the main memory is not supported on devices with less than 512 free bytes of SRAM.
However, Appending data to the information segments is possible on all devices, as this only requires 64 bytes of free SRAM and the smallest amount of RAM you will find on a MSP430 is 128 bytes.
Since flash memory does not allow changes. The data must be read into ram, modified, and then the flash segment is erased and then the data is finally written back.
## Flash Protection
Along with the hardware flash protection, the EasyMSP Flash library also has two software keys, to make sure that you really intended to perform a flash operation.
Only one key is required if erasing a single segment or writing any data. Two keys are required if you are attempting to use flashNuke() or flashEraseMainMemory(), as both of these functions can leave MSP430 nonoperational.
## Calibration constants
The MSP430 stores important calibration data in the flash segment INFOA. If you choose to erase INFOA or use flashNuke(), please be aware that after the operation, the MSP430 will no longer be compatible with EasyMSP.
## Clock Control
The Flash controller requires a certain frequency range for flash erase and write operations. In devices without a dedicated flash oscillator, the Flash library will save the current clock settings, and then set the MCLK to 1Mhz. After the operation completes, the flash library will restore the previous clock settings.
No clock changes are made if the MSP430 is equipped with a dedicated flash oscillator.
# Appendix B – Code documentation
## Library Depends
- EasyMSP Core Library
- Watchdog Library
- BCS Library
## Code Remarks