Change Log
Change log for EasyMSP.

# 1.0.2
## Summary
EasyMSP 1.0.2 contains a large amount of updates, improvements, and bug fixes.
## Internal code optimization
I've took a look at some internal code, Most notability main() and setup code, and optimized it for both code size and speed. The NMI Handler for value line and F2 series devices was optimized as well.
## GPIO Port ISRs consolidated
The GPIO Interrupt Service routines have been consolidated into one handler. Both port1_isr() and port2_isr() interrupt requests now point to the new consolidated handler port_isr(). This change only currently applies to the value line and F2 series device families.
## GPIO Function renaming
Some GPIO functions have been renamed to avoid confusion.
setHigh() → pinHigh()
setLow() → pinLow()
togglePin → pinToggle()
readPin → pinRead()
setDriveStrength() → pinDriveStrength()
setPullUp → pinPullUp()
setPullDown → pinPullDown()
setPullOff → pinPullOff()
## Preprocessor Macro renaming
Most internal preprocessor macros are now appended with “_EM_”.
## MSP430F5529 Device support
The MSP430F5529 MCU is now supported with EasyMSP.
## Code organization
#### “core” sub-directory
EasyMSP now holds core source files in the new “core” sub-directory.
#### Source file splits
EasyMSP source files have been split into multiple files for better organization.
## Device files
Device files in “device” are in the process of being deprecated. Necessary information about a device can be obtained from the TI MSP430 header file.