Change Log
For EasyMSP 2.x.x

# EasyMSP 2.1.0
## Changes
### Run-time
NEW: Support for running a self check at boot of the MSP430's CPU, SRAM, and Flash.
NEW: Support for refreshing flash after certain amount of system boots.
NEW: Support for verifying the integrity of flash at boot.
NEW: Support for custom PANIC/EMERGENCY level error handing by user call back function.
### Driver/GPIO/port
NEW: PORT4 support.
NEW: Word (16 bit) width port support.
NEW: Word width functions portWordWrite(), portWordRead().
IMPROVED: Detection of available ports.

### Driver/Flash
NEW: Option to reserve a flash segment for run-time use. This requires EABI, and only works on TI's compiler. Sorry GCC users.
NEW: Option to use reserved segment as scratchpad for appending flash data at runtime for devices with insufficient amounts of SRAM. This is a costly operation.
NEW: Function to erase all flash, flashNuke().
RENAMED: flashErase() to flashEraseSegment().
IMPROVED: flashEraseSegment() logic, parameter passing.